## Slide 1: Flood Risk Seminar
Exercise with R
Xiaoxiang Guana, Bruno Merza,b
a. GFZ German Research Centre for Geosciences, Section Hydrology, Potsdam, Germany
b. Institute of Environmental Science and Geography, University of Potsdam, Potsdam, Germany

## Slide 2: Overview
Introduction to R
Exercise with R - Flood frequency analysis
Exercise with R - Time-varying flood risk analysis
Materials here:
https://github.com/XiaoxiangGuanGFZ/FloodRiskSeminar

## Slide 3
Accessing the data (getting the data into the application from multiple sources)
Cleaning the data (coding missing data, fixing or deleting miscoded data, transforming variables into more useful formats)
Annotating the data (in order to remember what each piece represents)
Summarizing the data (getting descriptive statistics to help characterize the data)
Visualizing the data (because a picture really is worth a thousand words)
Modeling the data (uncovering relationships and testing hypotheses)
Preparing the results (creating publication-quality tables and graphs)
Typical (successful) procedures for data science
Getting data in
Data manipulation
Visualization
Algorithm
Topic 1. Introduction to R

## Slide 4
Topic 1. Introduction to R
What’s R: Installation, IDE, Packages, Help files
Data types and structures in R
Getting data into R
Functions and Control structures
Data manipulation
Graphic tools

## Slide 5
Topic 1. Introduction to R
1. What’s R
Key advantages of R:
Free of charge
Cross-platform
Open source
Interactive programming
Statistical facilities
Graphics capabilities

## Slide 6
Topic 1. Introduction to R
R project (download and installation): https://www.r-project.org/
IDE: RStudio (https://posit.co/download/rstudio-desktop/)
Packages: https://cran.r-project.org/web/packages/available_packages_by_name.html
1. What’s R

## Slide 7
Topic 1. Introduction to R
2. Data types and structures
Data type | Example | Description
Real numbers | 0, 12.3, -32, 112, 5432.0 | Decimal value is called numeric in R, and it is the default computational data type.
Integer | 3, 66, 2346L | Here, L can help tell R to store the value as an integer.
Logical (boolean) | True, False | It is a special data type for data with only two possible values which can be construed as true/false.
Character | 'a', 'good', "TRUE", '35.4' | In R programming, a character is used to represent string values. We convert objects into character values with the help of as.character() function.
numeric
categorical

## Slide 8
Topic 1. Introduction to R
2. Data types and structures
Data structure
a way of organizing and storing data
1) Vector
one-dimensional arrays used to store collection data of the same data type
  Numeric Vectors (data type: numeric)
  Logical Vectors (data type: logical)
  Character Vector or text strings (data type: character)
2) Matrix
two-dimensional arrays to store collections of data of the same mode.
3) Array
similar to matrices but they can be multi-dimensional (more than 2D)
4) Data Frame
generalization of matrices where different columns can store different mode data.
5) List
ordered collection of objects, where the elements can be of different types

## Slide 9
Topic 1. Introduction to R
3. Getting data into R
Export: write.table()
Import: read.table()

## Slide 10
Topic 1. Introduction to R
4. Functions and Control structures
Function sources:
Built-in
Third-party packages
Self-defined
What’s function:
A function is a set of statements organized together to perform a specific task.
Funtion_name <- function(parameters) {
  … function body (commands chunk)
  … return ()
  }
Notes: A function is a set of statements organized together to perform a specific task. R has a large number of in-built functions and the user can create their own functions. In R, a function is an object so the R interpreter is able to pass control to the function, along with arguments that may be necessary for the function to accomplish the actions.

## Slide 11
Topic 1. Introduction to R
Exercises:
getting data into R and find data file here: data/Example_data.csv, use read.table() function
Check the dimensions of the imported data
How many years this data set covers? Starting year? End year?
Is there any missing data? (-99.9 indicates the missing value). If there is, how many missing values?
Derive the annual maximum discharge series
Estimate the mean value, standard deviation of annual maximum discharge series
Export the annual maximum discharge series into text file (.csv or .txt format) with write.table() function

## Slide 12
Topic 1. Introduction to R
4. Functions and Control structures
Control structures:
If-Else statements
Loops
Notes: The if...else statement executes two different codes depending upon whether the test expression is true or false.

## Slide 13
Topic 1. Introduction to R
4. Functions and Control structures
Control structures:
If-Else statements
Loops
Notes: The if...else statement executes two different codes depending upon whether the test expression is true or false.

## Slide 14
Topic 1. Introduction to R
4. Functions and Control structures
While-type loop
keep looping as long as a specific logical condition is satisfied
Example:
i <- 0
while (i <= 4)
{
i <- i + 1
print(i)
}
## [1] 1
## [1] 2
## [1] 3
## [1] 4
## [1] 5
Control structures:
If-Else statements
Loops
Notes: While loop:
Keep execute some codes as long as the test expression is true.
Here the loop will only continue to pass values to the main body of the loop (the expression body) when i is less than or equal to 4 (specified using the <- operator in this example). Once i is greater than 4 the loop will stop.

## Slide 15
Topic 1. Introduction to R
4. Functions and Control structures
For-type loop
repeat a task a defined number of times:
Example:
for (i in 1:5) {
print(i)
}
## [1] 1
## [1] 2
## [1] 3
## [1] 4
## [1] 5
i <- 1
print(i)
## [1] 1
i <- 2
print(i)
## [1] 2
i <- 3
print(i)
## [1] 3
i <- 4
print(i)
## [1] 4
i <- 5
print(i)
## [1] 5
Control structures:
If-Else statements
Loops

## Slide 16
Topic 1. Introduction to R
1982 1 1 0 1.3 38.3
1982 1 2 0 0.6 37.8
1982 1 3 1.59 0.6 38
1983 1 1 0 0.4 41.5
1983 1 2 0.01 0.8 39.8
1983 1 3 0 1 38.3
1984 1 1 0 0.7 16.8
1984 1 2 0 1 16.3
1984 1 3 0 0.9 15.8
1985 1 1 0.22 0 20
1985 1 2 2.83 0.3 22.4
1985 1 3 0.04 0.4 24.9
1986 1 1 0 1.9 38
1986 1 2 0 1.7 27.8
1986 1 3 0.06 0.3 25.7
1987 1 1 0 1.7 9.6
1987 1 2 0 2.5 9.4
1987 1 3 0.22 1.4 9.2
1988 1 1 0 1.7 35.5
1988 1 2 0 0.9 34.2
1988 1 3 0 0.2 33.1
1989 1 1 0.12 1.6 52.6
1989 1 2 0.01 91 33.7
1989 1 3 0.42 0.6 30
Year month day rainfall evaporation discharge
…
…
…
…
…
…
…
…
y rainfall
1982 1797.59
1983 1650.93
1984 1373.37
1985 1390.72
1986 1282.76
1987 1660.45
1988 1693.15
1989 1586.80
Apply function sum()
aggregate(rainfall~y, data = df, FUN = sum)
5. Data manipulation

## Slide 17
Topic 1. Introduction to R
6. Graphing tool
https://r-graph-gallery.com/
Built-in
ggplot2: https://ggplot2-book.org/

## Slide 18
Topic 1. Introduction to R
6. Graphing tool
title
data
x-axis
y-axis
x-axis label
tick
Plot panel
Plot area
legend
tick label
y-axis label

## Slide 19
Topic 2. Exercise with R - Flood frequency analysis
Parameter:
ξ: Shape
µ: Location
σ: Scale
Cumulative distribution function
Cumulative distribution function
Probability density function

## Slide 20
Topic 2. Exercise with R - Flood frequency analysis
Exercises:
get data into R: ./data/Example_data.csv, use read.table() function
Derive the annual maximum discharge series
Estimate the GEV parameters for annual maximum discharge
Generate 100 random numbers based on the estimated GEV parameters

## Slide 21
Topic 2. Exercise with R - Flood frequency analysis
Flood risk analysis
Components:
Hazard
Exposure
Vulnerability

## Slide 22
Topic 2. Exercise with R - Flood frequency analysis
H: water level (m)
Q: discharge (m3/s)
Exercise:
In case, the flood defense water level is 3.8 m, then a flood happens, with the discharge of 11000 m3/s, what is the expected economic loss?
In case, the flood defense water level is 3.8 m, generate 100 years of GEV-distributed annual maximum discharge series, calculate the mean annual expected economic loss.
Design the which could keep the mean annual expected economic loss no greater than 1.5 million $ for the following 100 years.
Exceeding water level :
<=0.15 m loss: 0 (zero)
0.15~1 m loss:
>=1 m loss:
Notes: For instance, there is a city located beside the river and protected by embankments.
Within the river channel, the water level can be estimated from discharge.
Therefore, based on the water level – discharge relation, when a big discharge comes, we can derive the expected water level and quantify whether the water level will exceed the design defense level (flooding threshold) and the flood overtops or breaches the embankments and causes damages.
And further, the damages resulted from flood inundation is assumed to the function of exceeding water level.

## Slide 23
Topic 4. Exercise with R - Time-varying flood risk analysis